## Slide 1: Geothermal & Tidal Energy
-Tanmay Bhujade(20BCE10354)
-Suraj Pratap Singh(20BCE10279)
-Muskan Jain(20BCE10020)
-Shlok Mathur(20BCE11057)
-Siddharatha Chatterjee(20BCE10820)
-Saurabh Prakash(20BCE11005)
-Madhav Gupta(20BCE10020)
-Prashant Kumar(20BCE10033)

## Slide 2: Geothermal Energy
Geothermal energy is the thermal energy in the Earth's crust which originates from the formation of the planet and from radioactive decay of materials in currently uncertain but possibly roughly equal proportions.
Depending on its characteristics, geothermal energy can be used for heating and cooling purposes or be harnessed to generate clean electricity.
For electricity, generation high or medium temperature resources are needed, which are usually located close to tectonically active regions.

## Slide 3: Working
Hot water is pumped from deep underground through a well under high pressure.
When the water reaches the surface, the pressure is dropped, which causes the water to turn into steam.
The steam spins a turbine, which is connected to a generator that produces electricity.
The steam cools off in a cooling tower and condenses back to water.
The cooled water is pumped back into the Earth to begin the process again.

## Slide 5: Types of Geothermal Power Plant
Binary cycle power plants
Dry steam power plants
Flash steam power plants

## Slide 6: Binary Cycle Power Plant
This geothermal power plant is advantageous compared to the flash steam and dry steam power plants because it requires slightly cooler water (as low as 57°C (135°F) to heat a separate fluid (binary fluid) that has a lower boiling point.
The power plant enables cooler geothermal reservoirs to be utilized than is necessary for the flash steam and dry steam power plants.

## Slide 7: Dry Steam Power Plant
Dry steam is, essentially, water vapor or water in gaseous state. The geothermal power plant companies drill two separate wells to the extremely hot water reservoir under the earth’s surface; the production well and injection well.
The steam turns the turbine, which turns a shaft connected to a generator. With the turning, the generator converts the energy into electricity, which goes through power lines to a power grid and eventually supplied to homes, institutions, and industries.

## Slide 8: Flash Steam Power Plant
This kind of geothermal power plant utilizes water at temperatures of at least 182°C (360°F). As the name suggests, it uses flash steam to generate electricity.
Flash steaming is the process whereby extremely high-pressure hot water is flashed or vaporized into steam in a flash tank by reducing the pressure.
Flash steam power plants are the most common types of geothermal power plants in the modern world. The Wairakei Power Station, built in 1958 in New Zealand, was the first geothermal power plant that utilized flash steam.

## Slide 9: Uses
Technologies for direct uses like district heating, geothermal heat pumps, greenhouses, and for other applications are widely used and can be considered mature.
Many of the power plants in operation today are dry steam plants or flash plants (single, double and triple) harnessing temperatures of more than 180°C.
The United States is the largest producer of geothermal energy in the world, and hosts the largest geothermal field. Known as “The Geysers” in California, the field is spread over 117 square kilometers and formed of 22 power plants, with an installed capacity of over 1.5GW.

## Slide 10: Tidal Energy
Tidal power or tidal energy is harnessed by converting energy from tides into useful forms of power, mainly electricity using various methods. Although not yet widely used, tidal energy has the potential for future electricity generation. Tides are more predictable than the wind and the sun.
Tidal energy is created using the movement of our tides and oceans, where the intensity of the water from the rise and fall of tides is a form of kinetic energy.

## Slide 11: Working
Tidal barrages are low-walled dams, usually installed at tidal inlets or estuaries. ... During an incoming high tide, water flows over the turbines as the water rises. Then, the water flows back through the turbines as it becomes low tide. The turbines are connected to a generator which produces the electricity.

## Slide 12: Tidal Barrages
The barrage is one of the most popular tidal energy systems. A framework comparable to a dam, the barrage usually occupies the inlet of a lagoon or ocean bay that makes up the tidal reservoir.
This way, the tidal pool fills with the entering high tide and empties via an electric turbine structure with the exiting low tide. The most efficient type of system is a tidal power arrangement that goes both ways, as it produces electricity during the incoming and the outgoing tide.

## Slide 13: Tidal Turbine
Firstly, these are much like wind turbines in appearance. If installed on sea beds where the dial flow is the strongest, tidal turbines are most efficient.
For instance, a tidal facility may have negative effects on the ecosystems in the proximity of the tidal reservoir.
Tidal barrages, in particular, can influence the tidal levels in the basin, as well as increase the water’s turbidity (which represents the cloudiness of the water

## Slide 14: Why Do Tides Rise And Fall?
The tides--the daily rise and fall of the sea's edge--are caused by the gravitational forces between the earth, the moon and the sun. ... Since the moon is closer to our planet than the sun, it exerts a stronger gravitational pull on us.

## Slide 15: Future Of Geothermal Energy
Since geothermal typically provides base-load electric generation, integration of new power plants into existing power systems does not present a major challenge. Indeed, in some configurations, geothermal energy can provide valuable flexibility, such as the ability to increase or decrease production or startup/shut down as required.

## Slide 16: Future Of Tidal Energy
the future of tidal energy is tightly hinged to the costs involved. Right now, it’s difficult for tidal power to complete with the prices offered by traditional electric companies offering energy from traditional sources such as coal, oil and natural gas.
That said, the future looks brighter than ever before. Costs are coming down thanks to scientists’ shift toward more efficient underwater turbines and revamped logistics.
Plus, power generators are finding ways to preserve biodiversity by fashioning generators which can be placed farther out in the water and in locations that pose less of a risk to marine life.

## Slide 17
End